# HV Plate Processing Procedures

# (10/30/00)

- Visually inspect kapton for damages, excessive glue …

- HV test 3kV, 3 sec island scan

- Remove resistors next to the kapton bent

- Bend kapton – see kapton bending procedures

- Remove excessive glue

- Inspect traces for cracking

- Solder resistors

- Resistance test from kapton connector to hv pad (4.7kohm)

- Socket fitness test

- HV test 3KV island scan

- Ultra sound clean in isopropyl alcohol